## Slide 1: ECOFLOW AUTOMATED GARDEN IRRIGATION SYSTEM
Presented by :
Anisha Datta 20JE0137
Nahush Lele 20JE0519
Priyanshu Maurya 20JE0728
Satyam 20JE0871

## Slide 2: PROBLEM STATEMENT
Manual watering of plants often leads to under-watering or over-watering, affecting plant growth and health. This is especially problematic for individuals who are busy or frequently away from home. With the increasing need for water conservation, an automated system can provide a solution that optimally manages plant watering by measuring soil moisture and delivering water only when required.

## Slide 3: OBJECTIVES
To develop an automated irrigation system for potted plants or small gardens using soil moisture sensors.
To minimize water wastage and ensure plants receive adequate water based on soil conditions

## Slide 4: OUTCOME
A functional and cost-effective automated watering system that uses soil moisture levels to trigger irrigation, improving convenience and water conservation for garden owners.

## Slide 5: Components Required
Arduino UNO R3
5V Relay Module
Soil Moisture Sensor
Water Pump & Pipe

## Slide 6: Components Required
Soil Moisture Sensor
Purpose: Detects the moisture level in the soil and outputs an analog voltage proportional to that moisture level
.Connection Needs: Requires a power source (5V), a ground connection, and an analog output pin to send the moisture data to the Arduino.
Water Pump & Pipe
Purpose: Delivers water to the garden when activated.
Connection Needs: Is connected to the relay’s switching mechanism to receive power only when the relay is activated.

## Slide 7: Components Required
5V Relay Module
Purpose: Functions as a switch to control the water pump. Since the water pump may require more current than the Arduino can directly provide, the relay safely isolates and controls the higher-power circuit.
Connection Needs: Receives a digital control signal from the Arduino and connects to both the power source and the water pump circuit.
Arduino UNO R3
Purpose: Acts as the brain of the system. It reads the sensor data, decides whether watering is needed, and then sends a control signal.
Connection Needs: Has analog inputs (for reading sensor data) and digital outputs (for controlling the relay).

## Slide 8: Working of the Project
The sensor continuously monitors soil moisture.
The Arduino reads the sensor’s analog output and compares it to a predefined threshold.
If the soil is too dry (below the threshold), the Arduino sends a digital signal to the relay.
The relay then closes the circuit, powering the water pump to water the plants
Once the soil reaches an adequate moisture level, the Arduino stops the signal, the relay opens, and the pump turns off.

## Slide 9: THANK YOU